## Slide 1
ZeroFlush: A CSD-Native LSM Store with
In-Storage Write Path Organization
[Author Names]
[University / Lab]
[Target Venue: FAST / OSDI / ATC]
Notes: REVIEW: Title uses "CSD-Native" to signal architectural redesign, not just offloading. Consider alternative: "Flush-Free LSM". Venue TBD - FAST is ideal fit.

## Slide 2
Outline
1. Background: The LSM-tree Write Path and Its Costs
2. Motivation: Three-Way Organization Redundancy
3. Philosophy: Write Once, Organize In-Place
4. Challenges of a CSD-Native Write Path
5. ZeroFlush Design (WAL Partitioning / WAL=L0 / Partition Index / CSD Compaction)
6. Expected Results and Experimental Plan
7. Conclusion and Open Questions
2

## Slide 3
1. Background: The LSM-tree Write Path
Every Put(key, value) is organized THREE times:
1) WAL append (durability) - sequential write to NAND
2) MemTable insert (ordering) - skiplist / B-tree in DRAM
3) Flush (encoding) - sort + encode + build index + bloom filter
-> writes L0 SSTable to NAND
The same data crosses the PCIe bus 3 times and is written to NAND 3 times.
WAL write (1x) + Flush write (1x) + Compaction write (1x) = 3x write amplification
3
Notes: REVIEW: "3x write amplification" needs precise definition. Strictly: WAL(1x) + flush(1x) = 2x before compaction. Compaction is separate. Say "the write path touches NAND 3x" rather than "3x WA" to avoid reviewer pushback. WA is conventionally measured as total_bytes_written / user_bytes_written across the FULL lifecycle including compaction.

## Slide 4
1. Background: L0 Overlap and Write Stall
Flush produces L0 SSTables whose key ranges OVERLAP:
- MemTable fills by TIME, not by key range
- Each flush dumps whatever keys arrived -> cross-cutting ranges
Consequences of L0 overlap:
- Point queries must check ALL L0 files (read amplification)
- L0->L1 compaction must merge many overlapping files
- If compaction cannot keep up -> write stall (foreground blocked)
In RocksDB benchmarks: write stall can reach 1230s under write-intensive workloads.
L0 overlap is the "original sin" of the flush mechanism.
4
Notes: REVIEW: The 1230s stall number comes from AegonKV paper Table 1 (RocksDB, YCSB-A). Cite explicitly. Logic is sound: overlap -> read amp -> more compaction -> stall. But note: write stall is primarily caused by L0 file count exceeding slowdown/stop triggers, not directly by overlap per se. Overlap makes compaction heavier, which indirectly causes stall. Make this causal chain explicit.

## Slide 5
2. Motivation: Three Organizations for Three Purposes
Root cause: the write path serves three INDEPENDENT purposes
with three SEPARATE mechanisms:
WAL
Purpose: durability
Format: append-only log
Cost: 1x NAND write + PCIe
MemTable
Purpose: ordering
Format: skiplist in DRAM
Cost: 64-256MB memory + CPU
Flush
Purpose: encoding
Format: SSTable blocks + index
Cost: 1x NAND write + PCIe + CPU
If the storage device can compute, ordering and encoding
do not need the host. These three can collapse into ONE write.
5
Notes: REVIEW: This is the strongest slide in the deck. The "three organizations" framing is the key insight. However, a reviewer may argue: "WAL is not really organizing - it is just appending." Counter: WAL does impose a sequential order (by time), which IS a form of organization. But be prepared to defend this framing. Alternative: say "three data movements" instead of "three organizations" if the WAL point is challenged.

## Slide 6
2. Motivation: Why Does Flush Survive?
Prior work optimizes WITHIN the inherited write path; none re-derives it. Observation 1 - Overlap is decided at write admission MemTable fills by time, so flush emits overlapping L0 files; every prior work mitigates the cost at compaction time. None intervenes at admission. Observation 2 - Flush persists on an obsolete hardware premise The write path assumes ordering/encoding is possible only in host DRAM. Device compute breaks that premise, yet no design re-derives the path from it. Observation 3 - Offloading accelerates work; it cannot eliminate it CSD offload makes background work faster, but cannot remove the flush NAND write pass or the overlapping L0 it emits. Its benefit is bounded by the pipeline. ZeroFlush asks whether device compute makes the flush stage itself unnecessary accelerate vs. eliminate - a difference in problem definition, not in combination.
6
Notes: REVIEW (updated 08-03): Restructured from the generic "No Existing Work Addresses Both" template to an assumption-challenge framing with three observations. Slide logic chain: (1) Observation 1 = L0 overlap is decided at write admission (MemTable fills by time), not at compaction time - no prior work intervenes at admission. This is the most mechanism-specific claim. (2) Observation 2 = the flush stage survives on an obsolete hardware premise (ordering/encoding only in host DRAM); device compute breaks the premise but no design re-derives the write path from it. (3) Observation 3 = offloading accelerates work but cannot eliminate it - structural benefit upper bound. Defensive notes: Obs 2 requires evidence that the "host-only ordering" assumption is actually obsolete - the four ZeroFlush mechanisms (WAL partitioning, WAL=L0, partition index, CSD compaction) are the constructive proof. Obs 3 anticipates the reviewer challenge "elimination is just an extension of offloading" - the answer is the NAND write-count difference: offload keeps 3 NAND touches, eliminate achieves 2. Keep the closing line as the positioning anchor: accelerate vs eliminate = problem-definition difference, not combination. Related-work coverage intentionally compressed to one framing line ("prior work optimizes WITHIN the inherited path") rather than per-system bullet lists; the detailed per-system comparison belongs in the Related Work slide if added, or the paper body. If reviewers want named systems (WiscKey/Titan/BlobDB/FPGA-Compaction/AegonKV/PinK), answer verbally from this list rather than cluttering the slide.

## Slide 7
3. Philosophy: Write Once, Organize In-Place
Write once, organize in-place.
Data is written to NAND exactly once (as WAL).
All subsequent organization (ordering, encoding, merging)
happens inside the storage device, on the internal bus.
CSD is not an accelerator. It is an enabler of a new write path.
Traditional view: Host organizes -> CSD stores
ZeroFlush view: Host writes -> CSD organizes in-place
This distinction is what separates "offloading" from "restructuring".
7
Notes: REVIEW: This is the "philosophy slide" - keep it conceptual, no implementation details. The reviewer should leave this slide thinking "OK, this is a different way of thinking about LSM, not just an engineering tweak." Risk: some reviewers dislike philosophy slides as "hand-waving." Mitigate by making the next slides very concrete.

## Slide 8
4. Challenges of a CSD-Native Write Path
Eliminating flush and reorganizing in-storage sounds ideal, but:
(1) Ordering gap
WAL is append-only (unordered).
SSTable requires sorted keys.
Sorting on FPGA is expensive
(external sort needs DRAM).
Cannot just "write and forget".
(2) Resource limits
FPGA DRAM: only ~4 GB.
CU count: bounded by LUT/FF.
Large WAL segments must be
processed in bounded chunks.
Unbounded input -> device crash.
(3) Host-device sync
Host needs metadata back
(new SSTable info, key range).
Version conflicts: concurrent
writes during compaction.
Coordination without stalling.
ZeroFlush answers: (1) Partition index turns sort into seq-read | (2) Bounded partitions + CU scheduling | (3) One-shot index push + lazy validation
8
Notes: REVIEW: Mirror AegonKV slide 7 structure (3 challenges -> 3 answers). The "ordering gap" is the hardest challenge - this is where the partition index innovation lives. Make sure the answer preview at the bottom is visible but not dominant.

## Slide 9
5. ZeroFlush: System Overview
Host side (redesigned):
- No MemTable. Replaced by lightweight Partition Index.
- WAL written in partitions aligned to L1 key ranges.
- Each WAL partition IS an L0 SSTable (no flush needed).
- Small write cache (few MB) for hot reads.
SmartSSD side (new):
- CSD Merge Compaction Engine on FPGA.
- Reads WAL partition by index order (no sorting).
- Streaming merge with L1 SSTable -> new L1.
- P2P channel: all data movement stays inside SSD.
Philosophy: software-hardware synergy. Host writes once; CSD organizes.
9
Notes: REVIEW: Need a system architecture figure here (Fig. 4 equivalent). Draw Host (WAL partitions + Partition Index + Write Cache) and SmartSSD (CSD Compaction Engine with P2P path). Without a figure this slide is too text-heavy. TODO: create figure.

## Slide 10
5. Design (1): WAL Partitioning by L1 Key Ranges
Each Put(key, value) is routed to a WAL partition:
partition_id = range_lookup(key, L1_boundaries)
WAL is no longer a single append-only log.
It is N parallel logs, one per L1 key range:
WAL_0: keys in [a, f) WAL_1: keys in [f, k)
WAL_2: keys in [k, p) WAL_3: keys in [p, z)
Why this matters:
- Each partition maps to a NON-OVERLAPPING key range
- L0 overlap is eliminated at the source
- Compaction becomes partition-aligned (one partition -> one L1 region)
Overhead: one range lookup per Put (< 10ns with a small B-tree of boundaries).
10
Notes: REVIEW [LOGIC ISSUE]: L1 key ranges CHANGE after compaction (splits/merges). When L1 boundaries shift, existing WAL partitions may no longer align. Need to address: (a) how to handle boundary changes - freeze old partitions and start new ones? (b) what happens to in-flight partitions during rebalancing? This is a significant gap. Suggest: treat L1 boundaries as "soft" - partitions are created against current boundaries and remain valid even if L1 later splits. The CSD compaction handles the mismatch by doing a proper merge regardless of exact boundary alignment.

## Slide 11
5. Design (2): WAL = L0 (Flush Eliminated)
Traditional path:
Put -> WAL (NAND write #1) -> MemTable -> Flush -> L0 SSTable (NAND write #2)
ZeroFlush path:
Put -> WAL partition (NAND write #1) -> [partition IS the L0 SSTable]
Write amplification: 3x -> 2x (flush write eliminated).
What changes:
- No MemTable (replaced by partition index, ~40B/entry)
- No flush thread (no CPU for sort + encode + write)
- No flush I/O (no PCIe, no NAND write)
- L0 is born non-overlapping (from partitioning)
What stays the same:
- WAL still guarantees durability (append-only, sequential)
- Crash recovery: re-scan WAL partitions (no MemTable rebuild needed)
11
Notes: REVIEW [LOGIC ISSUE]: Calling an unordered WAL partition an "L0 SSTable" is a stretch. SSTable implies sorted + encoded + indexed. WAL partition is none of these. Two options: (a) define a new term "WAL-SSTable" or "raw L0" and be explicit that it lacks sort/encoding; (b) have CSD add minimal encoding (block headers) at write time so it is closer to SSTable format. Option (a) is more honest. The key claim should be "flush is eliminated" not "WAL is SSTable" - the format conversion happens during CSD compaction, not at write time.

## Slide 12
5. Design (3): Partition Index
Per-partition sorted index maintained in host memory:
entry = (key, wal_offset, seq_number) ~40 bytes
What it replaces:
MemTable (skiplist storing full KV): 64-256 MB
Partition Index (pointers only): ~2-10 MB
Memory reduction: ~96%
How it enables CSD compaction:
- Push index to CSD once at compaction trigger (~few MB)
- CSD reads WAL entries IN INDEX ORDER -> sorted output stream
- Sorting is replaced by sequential random reads
- CSD internal P2P random read: < 10 us, no PCIe
Read path:
Get(key) -> check partition index -> read WAL at offset
Hot keys: served from write cache (few MB LRU)
12
Notes: REVIEW [LOGIC ISSUE]: The "sort becomes seq-read" claim needs nuance. Index-order reads are RANDOM reads on NAND, not sequential. Random read throughput (~1.5 GB/s) is lower than sequential (~3.5 GB/s). For a 64MB partition with 60K entries, random reads take ~40ms vs sequential ~18ms. The advantage is NOT speed - it is DRAM savings (O(1) vs O(n)) and FPGA simplicity (state machine vs sort network). Frame it correctly: "eliminates the need for sorting logic and large DRAM buffers" rather than "faster than sorting."

## Slide 13
5. Design (4): CSD Merge Compaction
Trigger:
Host pushes partition index + L1 SSTable metadata to CSD
One PCIe transfer (few MB), then CSD runs autonomously
CSD pipeline (FPGA):
Stage 1: P2P Read WAL partition (by index order) -> sorted KV stream
Stage 2: P2P Read L1 SSTable (sequential) -> sorted KV stream
Stage 3: Two-way merge (compare keys, dedup by seq_number)
Stage 4: Encode new L1 SSTable (blocks + index + bloom filter)
Stage 5: P2P Write new L1 SSTable to NAND
Zero PCIe for data. Zero host CPU for sort/merge/encode.
Completion:
CSD returns metadata (new SSTable key range, size, bloom filter)
Host atomically swaps L1 pointer. Old files marked for deletion.
13
Notes: REVIEW: This is the FPGA Compaction (FAST 20) comparison point. Key differences to emphasize: (1) FAST 20 assumes BOTH inputs are sorted SSTables; you handle an UNORDERED WAL partition via index-guided reads. (2) FAST 20 is a bolt-on accelerator; your compaction is the ONLY path from L0 to L1 - there is no host-side fallback. (3) Your pipeline includes dedup by seq_number (version resolution), which FAST 20 does not need. Need FPGA resource estimate: merge comparator + encoder is much simpler than sort network, so more CUs can fit.

## Slide 14
5. Write Path: Traditional vs ZeroFlush
Traditional (RocksDB)
Put -> WAL append [NAND 1x, PCIe 1x]
-> MemTable insert [CPU sort, 64-256MB]
-> Flush [NAND 1x, PCIe 1x, CPU encode]
-> L0 SSTable (overlapping)
-> L0-L1 Compaction [NAND 2x, PCIe 2x, CPU merge]
NAND writes: 3x (WAL + flush + compaction)
PCIe traffic: 4x data crossings
CPU: sort + encode + merge
Memory: 64-256 MB MemTable
L0 overlap: YES
Write stall: possible
ZeroFlush
Put -> WAL partition append [NAND 1x, PCIe 1x]
-> Index update [CPU O(log n), ~40B/entry]
-> [partition IS L0, no flush]
-> CSD Compaction [NAND 2x, PCIe 0x, CPU 0]
NAND writes: 2x (WAL + compaction)
PCIe traffic: 1x data crossing
CPU: index update only
Memory: 2-10 MB index + few MB cache
L0 overlap: NO (partition-aligned)
Write stall: eliminated (CSD async)
14
Notes: REVIEW: This comparison table is the money slide. But verify the NAND write accounting: Traditional = WAL(1x) + flush(1x) + compaction read(1x) + compaction write(1x) = 3 writes + 1 read. ZeroFlush = WAL(1x) + compaction read(1x) + compaction write(1x) = 2 writes + 1 read. The "3x vs 2x" is about WRITES only. Be precise in the paper: "eliminates one full NAND write pass (the flush)." PCIe: traditional has WAL write + flush write + compaction read + compaction write = 4 crossings. ZeroFlush has WAL write + (index push, negligible) = ~1 crossing. This is correct.

## Slide 15
6. Expected Results and Experimental Plan
Testbed:
2x Intel Xeon Gold 5220, 64GB DDR4, Samsung SmartSSD (Xilinx UltraScale+ FPGA)
Baselines:
RocksDB (traditional), Titan (KV-sep, Direct GC), ZeroFlush w/o CSD (host-side)
Workloads:
YCSB A-F (zipfian, 200M ops), Twitter traces, Social Graph
Expected outcomes:
Throughput / Latency
Write throughput close to Titan w/o GC
(no flush overhead, no stall)
P99 latency: bounded by CSD async
Read: +write cache for hot keys
Write Amplification / Space
NAND write amp: 3x -> 2x (flush eliminated)
PCIe traffic: -75%
Host memory: 64-256MB -> 2-10MB
L0 space: 0 (no separate L0 files)
15
Notes: REVIEW [QUALITY ISSUE]: No experimental data yet. This is acceptable for a proposal/early-stage presentation but NOT for a paper submission. Before submission: (1) implement a prototype (even software-only simulation of WAL partitioning + index); (2) run YCSB on RocksDB with modified flush path; (3) measure actual write amp, throughput, stall time. The "expected outcomes" must become "measured outcomes." Also: include a "ZeroFlush w/o CSD" baseline to isolate the benefit of WAL partitioning alone vs the full CSD pipeline.

## Slide 16
7. Conclusion and Open Questions
Contributions:
- Identifies three-way organization redundancy as root cause of write-path costs
- Proposes "write once, organize in-place" with CSD as first-class participant
- WAL partitioning + partition index: eliminates flush and L0 overlap
- CSD merge compaction: zero PCIe, zero host CPU for background reorganization
- Write amplification 3x -> 2x; write stall eliminated; PCIe traffic -75%
Open questions:
- L1 boundary changes: how to handle partition rebalancing after L1 split/merge?
- Read path: write cache hit rate under zipfian vs uniform distributions?
- CSD resource contention: compaction vs foreground SSD reads on shared NAND channels?
- Portability: tied to Samsung SmartSSD; CXL-based compute-storage as alternative?
- Crash recovery: WAL partitions are unordered; rebuild cost after power loss?
16
Notes: REVIEW: Open questions are honest and important. The L1 boundary rebalancing issue is the most critical - if not addressed convincingly, reviewers will reject. Suggest: add a "discussion" section in the paper showing that partition-boundary misalignment is handled gracefully by the merge step (CSD does a proper sorted merge regardless of exact boundary alignment, so slight misalignment only causes minor read amplification during compaction, not correctness issues).

## Slide 17
Thank You
17